# Space Elevator Cost Breakdown

The cost breakdown for the space elevator has been based on the actual or projected costs from existing programs whenever possible. In situations where reliable cost estimates can not be obtained based on existing programs the component costs are taken from existing programs and combined with estimated design and construction cost estimates. The following cost breakdown is for the full construction of a 20,000 kg capacity space elevator starting with a 10 to 20 cm wide initial cable which has lower risk.

Launch costs
To deploy the initial cable we are proposing, 40, 000 kg, and the deployment spacecraft will require four launches of the new Atlas V Heavy (26,000 kg payload to LEO). We considered launching our initial spacecraft on the shuttle but found we could more cost effectively launch in on expendable vehicles. This does however imply that the assembly in LEO will need to be autonomous or done at the ISS. The four launches will cost $250M each. Alternative launch vehicles have been considered, Delta IV, Proton, Energia, Ariane V, Shuttle, Shuttle-C and Saturn V, but each is either not in operation, light on payload capability or expensive.

Deployment spacecraft
The initial spacecraft will need to be split into packages that will fit on available launch vehicles, 26,000 kg. To minimize the risk of cable loss due to meteor damage we must launch the largest ribbon cable possible. To do this within the payload of available launch vehicles we are proposing to launch two ribbons independently, mate their end masses and deploy them together. Only the ends will be connected during deployment to reduce the differential stresses between the cables. The two ribbons will be joined into one wide ribbon by the first climber that ascends the set. The combined ribbons will have a mass of 44,000 kg, vary in width from 10 cm to 23 cm, support climbers up to 990 kg and have a statistical lifetime of three years.
The cables will be mounted on long, large diameter spools (2m dia x 3 m long) to fit into the Atlas V fairing (5m dia x 23.4 m long) and minimize the stresses on the cables. For the spool and mounting structure of each cable we have estimated a cost of $25M.
A magnetoplasmadynamic (MPD) propulsion system will be used to move the spacecraft from LEO to GEO and then impart the required angular momentum during deployment. MPD systems of 200kW have been constructed and we will require two identical systems of roughly this size. These are simple systems and estimates of less than $1M have been forwarded for them. We will budget $10M each for design, testing and construction.
The power for the spacecraft will come from a laser beaming system. This will require photovoltaic arrays with a 10 meter diameter, we have budgeted an array of twice this area, 150 m2. Optimally the cells will be GaAs but silicon could be used with loss in efficiency and additional thermal issues. GaAs photocells are currently expensive, $50k/m2, but with large scale production which we will require for this program the per unit cost should drop. With lower production costs or an advanced silicon cell we estimate that photovoltaic cell costs for our program could be $10k/m2. The cost of the photocells will be roughly $1.5M. In addition we have estimated $7M for the actual assembly of the arrays and associated deployment system.
The structural system of the spacecraft will be required to support the photocells, cable spool mounts, MPD engines and control hardware. The structures also need to be designed such that the four individual payloads can be quickly and easily autonomously combined on orbit into one large spacecraft. We have estimated $15M for design and construction of the spacecraft structures.
The two cable endmasses will need to join on-orbit, smoothly start deployment of the cable, transmit telemetry during deployment, soft land on Earth and act as a beacon to facilitate easy retrieval. This system is comparable to a small satellite with less requirements in some areas and more in others. We have estimated that the cost of the combined two endmasses to be $20M.
The last major segment is the control hardware. This is also very similar to what would be found on a conventional spacecraft. It will be responsible for attitude control, telemetry, deployment control and autonomous or tele-operated on-orbit assembly. Again, to duplicate a small spacecraft with these mission objectives we estimate that the cost will be about $50M.
Additional hardware will include the braking motors, thermal control blankets, wiring, etc. These costs will be a small fraction of our program and we have estimated that they will be less than $10M.
The design and coordination of the spacecraft assembly will require a well managed effort. The spacecraft we will require is not complex compared to many that have been built and flown but it is large which will add its own difficulties. We have estimated $100M for the design and assembly coordination.
On top of these estimates we have added a 100% contingency to the spacecraft construction. This contingency comes out to $254M.

The Cable
The cable for the elevator will be mass produced and have a mass of 750,000 kg. Mass production costs of carbon nanotubes (CNT) will be roughly $100/kg based on Mitsui estimates. A dedicated production facility for processing raw CNTs into finished ribbon cable will be required at a cost of $100M??? check this???. The interconnects on the cable will require a development and production facility and initial discussion with 3M give us an estimate of possibly $20M.
As with the spacecraft we have added a 100% contingency on the cable cost estimate, $195M.

The Climbers
The climbers, like the cable, will be a mass production enterprise. We will require 230 climbers during the construction stage and many more during operations. The climbers are fairly simple systems consisting of photocells for receiving the beamed power, DC electric motors, tread based drive, structures and control. The motors will be roughly $50k for each 100kW of drive power at least initially but future production could drop this cost. The photocells, as with our spacecraft, will be $10k/m2. The structure and control will amount to $200k per climber. These costs all assume some savings due to mass production.

Power beaming
To insure continuous operation the power beaming system will consist of three ocean-going stations for $100M each based on Sealaunch and Megafloat. Each station will have one or two lasers ($100M) and an associated set of optics ($125M) and an additional power generation system ($10M). One additional system may be set up on land, Mojave desert, to pump climbers at altitude. This will insure continuous operation even if one or two laser beaming systems are down for maintenance.

Anchor station
$100M plus $20M for modifications based on Sealaunch and Megafloat systems. The modifications will be for implementing a precision tension control system for the cable attachement.

Tracking station
@ $500M based on NASA report and One Hectre telescope. This system may be in operation for other uses and the required tracking data could be purchased if the system is operationally sound.

## Facilities
Additional facilities that will be essential are living quarters for the crew and visitors at the anchor station. This will be a separate floating platform with ample space for a small airport, houses and professional facilities. A functional platform at roughly 0.3 km2 would be roughly $200M based on the megafloat system. Additional facilities will be required at various other locations and the cost associated with these will be about $2M per year.

## Admin
7 years with 200 people at $150k average $210M – does not include personel associated with components above. These are people at different locations around the world to account for the coordination of the construction effort and conducting technical efforts. This cost will also cover tracking operations, admin, satellite intergration, business operations, and costs associated with regulatory compliance.

Cont.
We are still in the early stage of planning so some error in our estimates are to be expected. Because of this we have placed a additional 30% contingency on all costs ($1.44B).

## Total
$6.24B

If we take these costs and run them through a business scenario I get that at 500$/kg ($270/lb) and 5000 kg launched per day (on each of two cables) that within a few years the company could go public and net 500% return at a P/E ratio of 20. A higher P/E ratio, which could easily be expected could net twice this return.